## Slide 1
INSTRUMENTATION & IOT
Innovating Sustainable Solutions
Prepared by:
ASSOC. PROF. TS. DR. ANITA AHMAD
DR. MUHAMMAD ARIFF BIN BAHARUDIN

## Slide 2
Brief Intro

## Slide 3
THE 4 MAIN COMPONENTS OF IOT
Innovating Sustainable Solutions
Every complete IoT system integrates these four building blocks — from sensing the world to showing it to people.
→
→
→
1
Sensors & Devices
Collect data & act
Temp sensor
Camera
Smart bulb
MCU board
2
Connectivity
Carry data to the cloud
Wi-Fi
Bluetooth
Cellular / 5G
Ethernet
3
Data Processing
Turn data into insight
Cloud
Database
AI / ML
Analytics
4
User Interface
People see & control
Mobile app
Web app
Dashboard
Alerts
Source: DataFlair — “How IoT Works: 4 Main Components of an IoT System”

## Slide 4
IOT COMMUNICATION PROTOCOLS
Innovating Sustainable Solutions
1 Sensors
›
2 Connectivity
›
3 Processing
›
4 Interface
Communication protocols are the “languages” used inside the Connectivity layer — Component 2.
CATEGORY Application-layer (data / messaging) protocols
MQTT
Message Queuing Telemetry Transport
Publish / Subscribe · TCP
Lightweight pub/sub for constrained, unreliable networks.
HTTP / HTTPS
HyperText Transfer Protocol
Request / Response · TCP
Universal REST — simple and everywhere, but heavier.
CoAP
Constrained Application Protocol
Request / Response · UDP
REST-style for tiny low-power devices; maps to HTTP.
AMQP
Advanced Message Queuing Protocol
Message queue · TCP
Reliable queued messaging with delivery guarantees.
WebSocket
Full-duplex over one TCP socket
Full-duplex · TCP
Persistent two-way channel for real-time dashboards.
DDS
Data Distribution Service
Data bus (pub/sub) · UDP
Real-time data bus for industrial, mission-critical IoT.
How it stacks: these run over transport (TCP / UDP), which ride on the link/radio protocols — Wi-Fi, BLE, Zigbee, cellular, LoRaWAN — from the Connectivity component.
Sources: Arshon Inc.; Minew; HiveMQ — IoT communication protocols.

## Slide 5
WALKTHROUGH: IOT LIGHT MONITOR & LED CONTROL
Innovating Sustainable Solutions
ESP32 + HiveMQ Cloud + Node-RED
→
→
→
1
Sensors & Devices
Collect data & act
LDR
LED
ESP32
2
Connectivity
Carry data to the cloud
Wi-Fi
MQTT
3
Data Processing
Turn data into insight
Cloud
4
User Interface
People see & control
Web app

## Slide 6
MQTT Config

## Slide 7
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions

## Slide 8
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Register free account
https://www.hivemq.com/products/mqtt-cloud-broker/

## Slide 9
Innovating Sustainable Solutions
Use google.
SETTING UP MQTT - HIVEMQ

## Slide 10
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Create a serverless cluster

## Slide 11
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Select manage cluster

## Slide 12
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
This is the url that
you will use.
This is the port you
will use.
Overview tab.

## Slide 13
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Add credential.
Access Management
tab.

## Slide 14
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Set any username you
want.
Set any password you
want.

## Slide 15
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Select publish and
subscribe.
Password must be
same.
Save.

## Slide 16
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Credential created.

## Slide 17
SETTING UP MQTT - HIVEMQ
Innovating Sustainable Solutions
Username & Password same
as we set just now.
Must connect when we want
to use.

## Slide 18
Node-RED

## Slide 19
Node-RED Installation Guide
Innovating Sustainable Solutions
https://www.influxdata.com/blog/guide-installing-node-red/

## Slide 20
Node-RED RUN
Innovating Sustainable Solutions
sudo node-red
node-red
http://127.0.0.1:1880/
Once loaded, copy the IP address given and paste it into the browser.
Usually, the address is as follows:

## Slide 21
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions
Nodes
Flow
Configuration/Output

## Slide 22
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions

## Slide 23
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions

## Slide 24
https://github.com/xXMarifFXx/N-R_ESP32

## Slide 25
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions

## Slide 26
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions

## Slide 27
Node-RED FLOW INTERFACE
Innovating Sustainable Solutions

## Slide 28
ESP32

## Slide 29
ARDUINO IDE LIBRARY
Innovating Sustainable Solutions

## Slide 30
LIBRARY EXAMPLE
Innovating Sustainable Solutions

## Slide 31
INSERT YOUR INFO
Innovating Sustainable Solutions

## Slide 32
PRACTICE

## Slide 33
TASK 1
Innovating Sustainable Solutions
Familiarize with the interface and coding and get your IoT system started

## Slide 34
TASK 2
Innovating Sustainable Solutions
Use available components and build an interesting IoT System.

## Slide 35
Thank you
For more info about this report,
send an email to XXXXXXXXXX
16